## Slide 1: Digital Communication Project

## Slide 2
Name | ID
سيمون جوزيف شحاته عبدالملاك | 18010835
نورهان محمد جابر | 18012017
مارينا فؤاد عزيز | 18011310
يسرا ناصر شرف محمد | 18012095
ريم محمد عبد الكامل | 18010700
اسماء جمال عبدالحليم مبروك | 15010473
احمد محمد احمد عبدالجواد | 18010198
محمد طارق عامر | 1801505
احمد محمد ابوجبل | 18010200

## Slide 3
Part 1: ISI due to band-limited Channels

## Slide 4: Part 1: ISI due to band-limited Channels

## Slide 5: Defining variable

## Slide 6: To generate square pulses

## Slide 7: Generating the band limited channel

## Slide 8: Pulse shaping and channel

## Slide 9: Passing pulses through band channel

## Slide 10: Effect of band-limited channel on the two square pulses

## Slide 11: Effect of band-limited channel on the two square pulses
For nullifying the ISI terms, with an impulse of unit value applied at t=0 to the combined filters h(t) the samples of the h(t) at the output of the filter combination should be 1 at the sampling instant t=0 and zero at all other sampling instants kTb(k!=0) This is called Nyquist criterion for zero ISI.On the other hand, the signal that avoids ISI with the least amount of bandwidth is a sinc function that has zeros at t = Tb, 2Tb, 3Tb, … will also satisfy this condition.

## Slide 12
Sinc pulse shaping
Raised-cosine pulse shaping
Square-root raised-cosine pulse shaping

## Slide 13: Generate sinc pulses

## Slide 14: Sinc functions that ensures the criterion pulses of no ISI

## Slide 15: Passing through channel

## Slide 16: Effect of band-limited channel on the two sinc pulses pulses

## Slide 17: Optional part

## Slide 18: AWGN channel

## Slide 19: Adding noise to sinc

## Slide 21: To compute BER : first function “out”

## Slide 22: To compute BER :

## Slide 23: To compute BER :

## Slide 24: Part (2)
Inter-Symbol Interference due to multi-path channels

## Slide 25: Transmitter “Generating the signal BPSK”
Generating Random Integer between (0&1).
Converting every 0 to -1.
l = 100; %No of paths
S = randi([0,1],L,1);
A=length(S);
for i= 1 : length(S)
if S(i) == 0
S(i)= -1;
end
end

## Slide 27: Channel “Due to Multipath Effect & noise”
Generating the coefficients due to the multipath effect.
Adding the noise to the system.
h = MultipathChannel(L,1);
H = tril(toeplitz(h));
V = H * S;
Eb_No_db = 0; % The specified Eb/No value in dB
Energy_per_bit = 1;
No = Energy_per_bit/( 10^(Eb_No_db/10));
noise= (randn(size(V)) + 1i*randn(size(V)))*sqrt(No/2); %generate Noise
Y = (H * S) + noise ; %getting the received signal Y

## Slide 29: Estimating the output due to the channel effect
Taking the inverse of the input to the receiver.
Estimating the output of the signal if it is greater of “0” will be 1 if less than “0” will be -1.
Z= inv(H); %Equalize channel effect
X= Z * Y;
X_Estimated = zeros(l,1);
%Decision Maker
for i=1:length(S)
if X(i) > 0
B =1;
else
B=-1;
end
X_Estimated(i) = B; %Estimated_Transmitted_signal
end

## Slide 30: Changing the power ratio and calculate the BER
Changing the power of the noise.
Each time we calculate the BER.

## Slide 32: Another System to equalize the channel.
We can use the Adaptive Filters to generate the inverse of the channel.
We will use Weiner Solution.

## Slide 33
The idea behind the weiner:
  If the input is like figure(1), the filter will try to get the inverse of the channel like figure (2).

## Slide 34: Part 3: Comparisons of coding techniques

## Slide 35: In this project, we investigate the error correcting performance of different codes across a Binary Symmetric Channel (BSC) with a transition probability 0 ≤ 𝑝 ≤ 0.5. to assess the performance of these codes for different values of 𝑝
Repetation code – convolution code – polar codes

## Slide 36: Main script all the decoders n encoders will be illustrated in it’s part here is the general structure

## Slide 37: All Decoders are implemented inside this script

## Slide 38: All Decoders are implemented inside this script

## Slide 39: BSC

## Slide 40: Repetation code
In coding theory, the repetition code is one of the most basic error-correcting codes. In order to transmIn coding theory, the repetition code is one of the most basic error-correcting codes. In order to transmit a message over a noisy channel that may corrupt the transmission in a few places, the idea of the repetition code is to just repeat the message several times. The hope is that the channel corrupts only a minority of these repetitionsit a message over a noisy channel that may corrupt the transmission in a few places, the idea of the repetition code is to just repeat the message several times. The hope is that the channel corrupts only a minority of these repetitions
The chief attraction of the repetition code is the ease of implementation.
the minimum Hamming distance of the code equals its length . This gives the repetition code an error correcting capacity of errors in any code word)
. If the length of a binary repetition code is odd, then it's a perfect code.

## Slide 41: Here is a simulation for using repetation code for the transmitted data using matlab
Encoder
Very simple all about repeting every bit with L times as L=1/r :rrate
Decoder
Counts the L bits for each bit and decides upon than either it’s 0 or 1

## Slide 42: BER with p

## Slide 43: convolution code
is a type of error-correcting code that generates parity symbols via the sliding application of a boolean polynomial function to a data stream. The sliding application represents the 'convolution' of the encoder over the data, which gives rise to the term 'convolutional coding'. The sliding nature of the convolutional codes facilitates trellis decoding using a time-invariant trellis. Time invariant trellis decoding allows convolutional codes to be maximum-likelihood soft-decision decoded with reasonable complexity

## Slide 44: encoder

## Slide 45: Decoding
A Viterbi decoder uses the Viterbi algorithm for decoding a bitstream that has been encoded using a convolutional code or trellis code.
There are other algorithms for decoding a convolutionally encoded stream (for example, the Fano algorithm). The Viterbi algorithm is the most resource-consuming, but it does the maximum likelihood decoding. It is most often used for decoding convolutional codes with constraint lengths k≤3, but values up to k=15 are used in practice.

## Slide 46: decoder

## Slide 47: BER with P

## Slide 48: BER with P repetation -convolution

## Slide 49: POLAR Codes